## Slide 1: Single-Pixel Thermal Imaging Solution
Joshua Alexander
EECE 6038C - Advanced Microsystems
Spring 2016
Develop a low-cost thermal imaging system using a single-pixel, non-contact thermometer

## Slide 2: Background
Thermal image data is underutilized, many potential avenues
  Computer vision supplement
  Home efficiency audits
Existing thermal imaging solutions are very expensive
  Thermal sensor ICs alone are >$250 (FLIR development kits)
  Others do not offer true capture of medium wavelength infrared signals
Many applications do not utilize fast imaging techniques
  Low-refresh rates/low resolutions may be acceptable

## Slide 3: Design (Sensor and Gimbal)
Develop a low-cost thermal imaging using a single-pixel, non-contact thermometer
Melexis MLX90614 (MLX90614ESF-DCI-000-TU)
  5° FOV
  Resolution of 0.02°C
  Temperature range of -40°C to 85°C
Dual servo pan tilt mechanism to steer sensor

## Slide 4: Design (MCU)
Microchip 16-bit PIC MCU chosen (PIC24FJ128GB202-I/SP-ND
  I2C ability
  USB connectivity (for PC HID interface and debugging)
  PWM support (for servos)
  Six 10-bit ADCs
  128KB of program memory

## Slide 5: Design (Hardware Overview)

## Slide 6: Design (Firmware Logic)
All firmware code written in C
MPLAB X IDE used for development and in-circuit debugging

## Slide 7: Design (PCB)
All physical design done in Eagle CAD (schematic capture and layout)
Final dimensions: 39mm by 51.5mm
Reworks needed on laser diode footprint and micro USB connector

## Slide 8: Results
Final system capable of both user-guided thermal measuring and pre-defined scan patterns over a 180° half sphere
Linear mapping of temperature readings heatmap pixels

## Slide 9: Issues/Future Improvements
MLX sensor with narrow FOV is slow (long settling time)
  Issue when trying to quickly scan an area quickly
  Temperature transients seen from previous measurements
Use MLX sensor’s ambient temperature measurements to correct for systematic temperature reading errors
Move MLX sensor and laser to separate PCB
  Reduce load on gimbal
  Reduce heating effects from power supply and MCU
Implement projection of thermal imaging data on top of visible spectrum
  Additional camera sensor needed
Non-linear heatmap mapping of temperature readings to color

## Slide 10: Appendix